## Slide 1
Quantum Optimization for
Access Point Selection
Under Budget Constraint
Mohamed Khalil Brik¹ · Ahmed Shokry² · Moustafa Youssef¹
¹American University in Cairo · ²Pennsylvania State University
IEEE QCNC 2026 · April 6–8, Kobe, Japan

## Slide 2
What is Indoor Localization?
📍 You enter a hospital, airport, or warehouse. GPS doesn't work indoors. How does an app know exactly where you are?

## Slide 3
The Access Point Selection Problem
A modern building has hundreds of WiFi access points (APs). Using all of them is expensive and creates noise. Which APs should you keep?
Too Many APs → Problems
Redundant signals inflate database size
Matching is slower with more APs
Noisy APs hurt localization accuracy
High hardware & maintenance cost
Classical Selection is Slow
Optimal subset = NP-hard combinatorial problem
Greedy/PCA methods don't scale to 500+ APs
Exhaustive search of all combinations is infeasible
No budget guarantee on number of selected APs
Our Quantum Solution
Formulate as QUBO, solved by quantum annealing
Maximize AP importance (signal discrimination)
Minimize AP redundancy (correlated signals)
Enforce strict budget: select exactly k APs

## Slide 4
QUBO Formulation

## Slide 5
Importance Metric Comparison
Mean 3D Localization Error (m) — Lower is Better
✓ Entropy best captures location-discriminative signal variation. Shannon entropy measures RSS diversity across all fingerprint locations, directly aligned with what fingerprinting needs.

## Slide 6
Results: Quantum vs. Classical
96.1%
AP Reduction
(520 → 20 APs)
61×
Speedup over
Simulated Annealing
18.2%
Mean 3D Error
Reduction vs. SA
0.20 s
Time-to-Solution
(Quantum)
Performance Comparison
Method
APs Used
Mean 3D Error
Floor Accuracy
Time (s)
All APs
520
12.4 m
70.4%
—
Simulated Annealing
520
14.3 m
58.6%
12.28 s
Quantum Annealing ★
20
11.7 m
73.0%
0.20 s
★ Quantum annealing achieves best accuracy AND fastest runtime with fewest APs

## Slide 7
Floor Localization Accuracy
Floor Classification Accuracy (%)
Why QA
beats
All APs?
Removes
noisy APs
Minimizes
redundancy
Entropy-
guided
Quantum
tunneling

## Slide 8
Computational Speedup
61×
Quantum Annealing achieves a 61× speedup over classical Simulated Annealing same QUBO problem, same budget constraint
Annealing Time Comparison

## Slide 9
Conclusion
First QUBO formulation with a strict AP budget constraint for 3D indoor localization
96.1% reduction in required APs (520 → 20) with negligible accuracy loss
73% floor accuracy — outperforming classical SA (58.6%) and all-AP baseline (70.4%)
61× speedup: 0.20 s vs 12.28 s for simulated annealing
Entropy-based importance metric identified as optimal for fingerprinting workloads
Future Work: Real D-Wave hardware deployment · Multi-building 3D scaling · Journal fast-track (Digital Communications & Networks)

## Slide 10
Thank You
Questions & Discussion
Mohamed Khalil Brik
mohamedkhalil.brik@aucegypt.edu
American University in Cairo · Computer Science & Engineering
Website: khalilbriktn.github.io/personal-website/
IEEE QCNC 2026 · Kobe, Japan · April 6–8, 2026